## Slide 1: RAM(RANDOM ACCESS MEMORY)

## Slide 2: TYPES OF RAM
Static RAM: SRAM is random access memory that retains data bits in its memory as long as power is being supplied.

## Slide 3
Dynamic RAM: Dynamic random-access memory is a type of random access semiconductor memory that stores each bit of data in a separate tiny capacitor within an integrated circuit.

## Slide 4: TYPES OF DYANMIC RAM
SDRAM
DDR SDRAM
DDR2 SDRAM
DDR3 SDRAM
DDR4 SDRAM

## Slide 5: SDRAM
It stands for Synchronous Dynamic Random Access Memory.
SDRAM is designed to synchronize itself with the timing of the CPU.

## Slide 6: DDR SDRAM
The next generation of SDRAM is DDR, which achieves greater bandwidth than the preceding single data rate SDRAM by transferring data on the rising and falling edges of the clock signal.

## Slide 7: DDR2 SDRAM
Its primary benefit is the ability to operate the external data bus twice as fast as DDR SDRAM. This is achieved by improved bus signal.

## Slide 8: DDR3 SDRAM
DDR3 memory reduces 40% power consumption compared to current DDR2 modules, allowing for lower operating currents and voltages.

## Slide 9: DDR4 SDRAM
DDR4 SDRAM provides the lower operating voltage (1.2V) and higher transfer rate.

## Slide 10: DIFFERENCE BETWEEN SDRAM, DDR, DDR2, DDR3, DDR4

## Slide 11: DIFFERENCE BETWEEN DDR, DDR2, DDR3, DDR4

## Slide 12: TYPES OF RAM SLOTS
SIMM slot :
  SIMM RAM had to be installed at an angle and pushed upright into place.
DIMM slot :
  DIMM slots allow for straight-forward installation of memory modules.
RIMM slot :
  The module slots for RIMMs were physically similar to DIMM slots and the modules were installed in the same way.

## Slide 13: ROM(READ ONLY MEMORY)

## Slide 14: TYPES OF ROM
Masked ROM
PROM
EPROM
EEPROM
Flash ROM

## Slide 15: Masked ROM
It is also known as MROM. It is a static ROM which comes programmed into an integrated circuit by its manufacturer.

## Slide 16: PROM
It stands for Programmable Read Only Memory.
The data stored in it cannot be modified and therefore it is also known as one time programmable device.

## Slide 17: EPROM
It stands for Erasable Programmable ROM. It is different from PROM as unlike PROM the program can be written on it more than once.

## Slide 18: EEPROM
It stands for Electrically Erasable Read Only Memory.
These are also erasable like EPROM, but the same work of erasing is performed with electric current.

## Slide 19: Flash ROM
It is an updated version of EEPROM.
Flash memory provides this advantage over the EEPROM by enabling this feature of altering many locations simultaneously.